## Slide 1: FUNDAMENTALS OF GREEN CHEMISTRY
MODULE 2 - MORNING SESSION II
1-DAY PRESENTATION
www.greenchemistry-toolkit.org

## Slide 2: What is Green Chemistry?
Green chemistry is the design of chemical products and processes to reduce or eliminate the generation and use of hazardous substances.
Anastas, P. T., Warner, J. C. (2000). Green chemistry: Theory and Practice. New York; Oxford University Press.
Notes: Definition of the green chemistry: Green chemistry is the design of chemical products and processes that reduce or eliminate the use and generation of hazardous substances.
. The field was developed 25 years ago by Anastas and Warner, and presented in their seminal work “Green Chemistry: Theory and Practice”.

## Slide 3: THE FOCUS ON CHEMICAL DESIGN
The moment chemists initiate designing, they are making choices about the human health and environmental impacts of their product:
Design is intended
All characteristics, including performance and toxicity, can be designed
Image source: ChemDoodle Web Components

## Slide 4: THE CHEMICAL DESIGNING PROCESS
Ultimately determining the characteristics of the waste stream, energy requirement and the toxicity of the entire process.
DECISION MAKING
Type of resources
What materials (feedstocks, additives) are needed?
Are the materials readily available?
How much material is needed?
Manufacturing process
What technology is needed?
What is the scale of the experiment?
Ultimately determining the characteristics of the waste stream, energy requirement and the toxicity of the entire process.
Notes: Types of resources:
While the starting materials are important (feedstocks), at the design phase the decision on the solvents, additional reactants is also necessary.
Decision on the scale of the manufacturing process is needed. Each industry is different, for example a big pharma will have other scale than a startup.
All these decisions determine the characteristics of the waste streem, energy usage, and toxicity of the entire process.

## Slide 5: IT’S NOT JUST HOW YOU DESIGN BUT WHAT YOU DESIGN…
Chart: investments (i.e., time, money, resources,energy)
| 0 | 1 | 2 | 3 | 4 | 5
optimize the existing solution (incrementalism) | 0 | 0.2 | 0.35 | 0.45 | 0.5 | 0.55
re-engineer the system | 0 | 0.3 | 0.45 | 0.7 | 0.8 | 0.9
re-define the problem | 0 | 0.5 | 0.8 | 1 | 1.2 | 1.3
As the investments increase, so do the benefits. The largest benefit is when the company re-defines the problem and finds a novel solution.
Schematic of potential benefits vs. investments
Notes: Example:
Tesla has developed an electric car, which is independent of the petroleum (redefining a problem)
Nissan has optimized the battery so the car can run longer without charging (optimizing the existing solution)

## Slide 6: THE 12 PRINCIPLES OF GREEN CHEMISTRY
The principles address:
  Toxicity
    Reducing the hazard
  Feedstocks
    Use of renewable resources
  Designing safer products
    Non toxic products by design
  Biodegradability
    Enhancing breaking down at the end of life
  Energy
    Reducing the energy needs
  Accidents
    Eliminating accidents
  Efficiency
    Shorter processes and synthesis
Source: https://www.acs.org/content/acs/en/greenchemistry/what-is-green-chemistry/principles/12-principles-of-green-chemistry.html
Notes: Green chemistry is defined by 12 Principles, which address various topics. Most principles have tools or metrics associated to help the researcher and guide them through green chemistry improvements.

## Slide 7: TWELVE PRINCIPLES… ISN’T THAT HOW IT IS DONE NOW?
Entire industries are geared toward cleaning up after wasteful chemical syntheses
Today’s scientific literature is filled with synthetic pathways that are inefficient in terms of design
Reagents are seldom selected with regard to hazard
Industrial chemicals do not have minimal hazard as a performance criterion
Persistence of chemicals in the biosphere and in our bodies is a major global health issue (CDC 250 chemicals since 1945)
The vast majority of organic chemicals are made by depleting (non-renewable) feedstocks
Our chemical industry deals with safety through engineering and security through barricades.

## Slide 8: BENEFITS OF GREEN CHEMISTRY
For the environment:
  Products which will biodegrade and won’t persist in the environment
For human health:
  Products with won’t cause toxicity to humans
For the economy:
  Novel products which boost competitiveness
For sustainability:
  Products made from renewable resources
For science:
  New scientific knowledge

## Slide 9: GREEN CHEMISTRY ACROSS INDUSTRIAL SECTORS
Defense and aerospace
Adhesives
Coatings
Corrosion, inhibitors
Automotive
Solvents
Polymers
Fuels
Household cleaners
Surfactants
Fragrances
Dyes
Cosmetics
Builders
Chelating agents
Dyes
Agriculture
Pesticides
Fungicides
Fertilizers
Electronics
Solder
Housings
Displays
Pharmaceuticals
Defense and aerospace
Adhesives
Coatings
Corrosion, inhibitors
Automotive
Solvents
Polymers
Fuels
Household cleaners
Surfactants
Fragrances
Dyes
Cosmetics
Builders
Chelating agents
Dyes
Agriculture
Pesticides
Fungicides
Fertilizers
Electronics
Solder
Housings
Displays
Pharmaceuticals

## Slide 10: GREEN CHEMISTRY IS A FUNDAMENTAL CHANGE IN THINKING
Green Chemistry moves our consideration of how to deal with environmental problems from the circumstantial to the intrinsic.
Hazard must be recognized as a flaw in the designing process
Circumstantial
  Use
  Exposure
  Handling
  Treatment
  Protection
  Recycling
  Costly
Intrinsic
  Molecular design for reduced toxicity
  Reduced ability to manifest hazard
  Inherent safety from accidents or terrorism
  Increased potential profitability

## Slide 11: APPROACHING RISKS: EXPOSURE VS. SMART DESIGN
Green chemistry focuses on reducing risk by reducing hazard
If there is no hazard, exposure becomes irrelevant
The traditional approach to hazards focuses on reducing risk by minimizing exposure.
For example, wearing personal protective equipment or space ventilation if the chemical is volatile.

## Slide 12: THE TWELVE PRINCIPLES OF GREEN CHEMISTRY

## Slide 13: PRINCIPLE 1 It is better to prevent waste than to treat or clean up waste after it is formed.

## Slide 14: WHAT IS WASTE?
Anything that is is a leftover from the product/process and cannot be re-used.
Waste can be produced in any stage of a process life-cycle:
Origins of feedstock
Manufacturing
Distribution
Use
End of life

## Slide 15: WHEN IS A WASTE NOT A WASTE?
When the waste can be reused into another application where it becomes a feedstock.
When the wasted can be reduced or completely eliminated.

## Slide 16: PRINCIPLE 1: WASTE PREVENTION CASE STUDY: PHENOLS
Traditional method of obtaining phenols (drop-in platform chemicals) from petroleum.
Petroleum
Phenols (benzene, toluene, xylenes)
Production of phenols from biomass waste using depolymerization
Disadvantage: Not sustainable – dependent on depleting resources
Advantage: Uses abundant product (waste) as a starting material

## Slide 17: PRINCIPLE 1: WASTE PREVENTION CASE STUDY: DNTPS
Conventional production of deoxyribonucleotide triphosphates (dNTPs):
requires multiple steps and purifications
produces large amounts of hazardous solvent and reagent waste
Alternative synthesis:
a one-pot, three step sequence
eliminates the need for several hazardous reagents such as ZnCl2, triphenylphosphine, and solvents such as dimethylformamide and dichloromethane
E-factor improved by an order of magnitude
Solvent consumption reduced by 95%, hazardous waste by 65%, preventing 1.5 million tons of hazardous waste per year
Notes: dNTPs are essencial feedstock to perform Polymarase Chain Reaction (PCR)

## Slide 18: PRINCIPLE 2 Synthetic methods should be designed to maximize the incorporation of all materials used into the final product.

## Slide 19: PRINCIPLE 2: ATOM ECONOMY
Ideally all atoms from the reagents are incorporated into a final product
  High atom economy ↔ less waste production
There are no co-products or by products in the reaction
The molecular waste is therefore reduced

## Slide 20: PRINCIPLE 2: ATOM ECONOMY CASE STUDY: STYRENE
Traditional method of styrene production:
Disadvantages:
Use of benzene, a known carcinogen, as a starting material
High temperature (800-950 0C)

## Slide 21: PRINCIPLE 2: ATOM ECONOMY CASE STUDY: STYRENE
Styrene production from butadiene using Diels-Alder reaction
Advantages:
Diels-Alder reaction =100% atom economy
Use of non-toxic starting material

## Slide 22: PRINCIPLE 2: ATOM ECONOMY CASE STUDY: IBUPROFEN
Traditional synthesis of ibuprofen was inefficient
  6 stoichiometric steps
  <40% atom utilization

## Slide 23: PRINCIPLE 2: ATOM ECONOMY CASE STUDY: IBUPROFEN
Catalytic synthesis of ibuprofen using Green Chemistry
  3 catalytic steps
  80% atom utilization (99% with recovered acetic acid)
  BHC

## Slide 24: PRINCIPLE 3 Wherever practicable, synthetic methodologies should be designed to use and generate substances that possess little or no toxicity to human health or to the environment.

## Slide 25: PRINCIPLE 3: NON-TOXIC SUBSTANCES
Ideally, non-toxic substances are used to synthesize a chemical product.
Polycarbonate (thermoplastic polymer) has been made using phosgene, a chemical warfare agent.

## Slide 26: PRINCIPLE 3: NON-TOXIC SUBSTANCES CASE STUDY: POLYURETHANE
Disadvantages
Using isocyanides which cause skin and respiratory problems
When burned, they form toxic and corrosive fumes
Highly regulated by the US government
Traditional synthesis of polyurethane using isocyanides

## Slide 27: PRINCIPLE 3: NON-TOXIC SUBSTANCES CASE STUDY: POLYURETHANE
Advantages
No isocyanide is used in the synthesis.
Product is stable, and has increased resistance properties due to intramolecular hydrogen bonds.
Non-isocyanide synthesis of polyurethane using green chemistry
Hybrid Coating Technologies
Nanotech Industries

## Slide 28: PRINCIPLE 3: NON-TOXIC SUBSTANCES
Conventional paper bleaching: Chlorine dioxide (ClO2)
Disadvantages:
Produces unacceptable quantities of chlorinated pollutants, and many are exceptionally toxic.
Novel technology for paper bleaching with TAML/H2O2 using green chemistry.
Advantages:
Alternative catalytic breakdown of H2O2 to provide the oxidative equivalent
Lower temperature and time requirement

## Slide 29: PRINCIPLE 4 Chemical products should be designed to preserve efficacy of function while reducing toxicity.

## Slide 30: THE MODERN MOTTO OF TOXICOLOGY
“Everything is toxic. It is simply depends on the dose”
Often otherwise phrased as
“The dose makes the poison.”

## Slide 31: PRINCIPLE 4: REDUCE TOXICITY
Chemists can design chemicals which have reduced toxicity by:
Manipulation of chemical bonds, chemical functional groups
  Reactive functional groups have a greater potential to be toxic -> removing these groups is likely to reduce toxicity
Modification or termination of the biological pathway
  While difficult to achieve, if the chemical is modified not to interact with the biological pathway, no biological effect is triggered and the toxicity can be avoided.
Reducing or eliminating bioavailability.
  - If a chemical does not absorb into a body, it cannot cause harm.

## Slide 32: PRINCIPLE 4: REDUCE TOXICITY CASE STUDY: PESTICIDES
DDT - Dichlorodiphenyltrichloroethane - agricultural pesticide and a malarial control agent
DDT
Disadvantages
Carcinogenic
Threat to wildlife, especially birds- almost led to the extinction of a bald eagle population
Notes: DDT was used in the second half of World War II to control malaria and typhus among civilians and troops. After the war, DDT was made available for use as an agricultural insecticide and its production and use duly increased. Müller was awarded the Nobel Prize in Physiology or Medicine "for his discovery of the high efficiency of DDT as a contact poison against several arthropods" in 1948
Unfortunately it’s effect on birds was not tested. Research have shown that for certain species, DDT causes the thinning of eggshells which led almost to species extinction.

## Slide 33: PRINCIPLE 4: REDUCE TOXICITY CASE STUDY: PESTICIDES
Spinosad: a natural product for insect control
  Produced by bacteria Saccharopolyspora spinosa
  Isolated from Caribbean soil sample
  It targets insects nervous system
  Demonstrates high selectivity, low mammalian toxicity, and a good environmental profile
  Dow AgroSciences

## Slide 34: PRINCIPLE 5 The use of auxiliary substances (e.g. solvents, separation agents, etc.) should be made unnecessary wherever possible, and innocuous when used.

## Slide 35: TRADITIONAL SOLVENTS
Volatile Organic Compounds:
  Chloroform, carbon tetrachloride, methylene chloride, perchloroethylene (PERC)
  Benzene, Toluene, Xylene (BTX)
  Acetone, Ethylene Glycol, methylethyl ketone (MEK)
CFCs
Image source: Adobe Stock

## Slide 36: WHAT ARE THE CONCERNS FOR SOLVENTS?
Inherent toxicity
  Many of them are known carcinogens
Flammability
  Relatively low flash point and ignition point lead to high flammability profile
Explosivity
  They can easily explode causing harm
Stratospheric Ozone Depletion
  Decreasing ozone layer causes more radiation to reach the earth and causing skin cancers, cataracts, damage to immune systems, injury to plants, injury to marine organisms
Atmospheric Ozone Production
  Increasing Global Warming Potential

## Slide 37: GREEN CHEMISTRY SOLVENTS
Aqueous Solvents
  Solvents based on water and not organic solvents
Solventless Conditions
  Reactions done without solvents, for example, the ones used in mechanochemistry
Supercritical Fluids
  scCO2 which can evaporate after changing reaction conditions
Ionic Liquids
Notes: 22

## Slide 38: PRICINPLE 6 Energy requirements should be recognized for their environmental and economic impacts and thus should be minimized. Synthetic methods should be conducted at ambient temperature and pressure.

## Slide 39: PRINCIPLE 6: MINIMIZE ENERGY USAGE
Most energy is used for heating, cooling, separations and pumping.
Ideally, all reactions are performed at ‘ambient’ conditions – room temperature and atmospheric pressure – in order to minimize energy usage.

## Slide 40: PRINCIPLE 6: SYNTHESIS OF ATORVASTATIN
Atorvastatin, a cholesterol- lowering drug, suffers from high energy consumption as a result of 2 cryogenic reactions (-70oC)
New biocatalytic synthesis uses enzyme DERA and shortens the process by removing two energy intensive chemical steps.

## Slide 41: PRINCIPLE 7 A raw material or feedstock should be renewable rather than depleting wherever technically and economically practicable.

## Slide 42: RENEWABLE FEEDSTOCKS
CO2
Biomass (algae, corn, switchgrass, poplar, willow, sorghum, and bamboo)
Agricultural waste (ex. Manure)
Images from Adobe Stock

## Slide 43: BIOMASS PLATFORMS
Chart: Biomass production in nature: 180 billion metric tons/yr
| Carbohydrates | Lignin | Fats, proteins, terpenes, etc.
Sales | 75 | 20 | 5
Only about 4% utilized by humans
(food, ethanol, sweeteners)
Nature’s richest source of aromatic carbon. Used in polymers, adhesives, production of phenolic chemicals.
Converted into polymers, lubricants, and detergents.
Building blocks for a diverse chemical platform.

## Slide 44: PRINCIPLE 7: RENEWABLE FEEDSTOCKS CASE STUDY: CATECHOL SYNTHESIS
Synthesis of Catechol from D-Glucose using Green Chemistry
Traditional synthesis of Catechol using benzene
Notes: The new synthesis of catechol can be done from glucose rather than carcinogen.

## Slide 45: PRINCIPLE 7: RENEWABLE FEEDSTOCKS
Design and manufacture of new, high-performance bio-based materials
Many applications—resins, polymers, composites, and foams, and even circuit boards and a leather substitute
Derived from renewable, biological feedstocks such as chicken feathers, flax, vegetable oils, lignin, and cellulose
Manufacture process consumes less water and energy than conventional petroleum-based processes, produces less waste, and is industrially viable
Wool

## Slide 46: PRINCIPLE 8 Unnecessary derivatization (blocking group, protection/deprotection, temporary modification of physical/chemical processes) should be avoided whenever possible.

## Slide 47: PRINCIPLE 8: DERIVATIZATION
Substrate
Product
Substrate
Intermediate A
Intermediate B
Intermediate C
Intermediate D
Intermediate E
Product
Traditional approach
Green Chemistry approach
Notes: Whenever possible, limit number of steps and unnecessary transformations. Avoid the use of protecting groups as it requires extra reagents and generates more waste.

## Slide 48: PRINCIPLE 8: DERIVATIZATION CASE STUDY: 6-AMINOPENICILLANIC ACID
Synthesis of 6-aminopenicillanic acid – core moiety of penicillin
Traditional synthesis of 6-aminopenicillanic acid using 3 steps and intermediate products:
New synthesis using enzyme and less derivatives

## Slide 49: PRINCIPLE 9 Catalytic reagents (as selective as possible) are superior to stoichiometric reagents.

## Slide 50: PRINCIPLE 9: CATALYTIC REAGENTS
Catalysts can facilitate complex reactions by:
  Lowering the activation energy of the reaction
  Reducing temperature necessary to achieve a reaction
  Controlling the site of the reaction (selectivity enhancement)
Image source: Adobe stock
Notes: Catalysts lower the activation (threshold energy) in the reaction.

## Slide 51: PRINCIPLE 9: CATALYTIC REAGENTS CASE STUDY: NAPROXEN SYNTHESIS
Synthesis of Naproxen using Green Chemistry
  chiral transition metal complex
  97% yield in three steps
  Dartt and Davis

## Slide 52: PRINCIPLE 9: CATALYTIC REAGENTS CASE STUDY: PRODUCING PAPER
Polyoxometalate (POM) catalysts
  - non-toxic, inorganic cluster compounds
  - selectively delignify wood
  utilize only air and water
Converts trees to paper without the use or generation of toxic chemicals
  Hill, Emory University; Weinstock, USDA Forest Service

## Slide 53: PRINCIPLE 10 Chemical products should be designed so that at the end of their function they do not persist in the environment and break down into innocuous degradation products.

## Slide 54: PRINCIPLE 10: BIODEGRADABILITY CASE STUDY: PLASTICIZERS
Conventional plasticizers such as DiNP are a needed additive to soften plastics
Disadvantages:
DiNP exposure has been linked to liver toxicity, endocrine disruption and carcinogenicity
They are persisting in the environment

## Slide 55: PRINCIPLE 10: BIODEGRADABILITY CASE STUDY: PLASTICIZERS
Alternative plasticizers such as isosorbide diester made from starch
Advantages:
Offers 1 to 1 substitution of DiNP in plastics
Thermally stable and biodegradable

## Slide 56: PRINCIPLE 10: BIODEGRADABILITY CASE STUDY: PLASTICS
Conventional plastics (PET) are made from petroleum
Disadvantages
Will persist in the environment
Is made from depleting resources
high temperature
vacuum
catalyst
Petroleum

## Slide 57: PRINCIPLE 10: BIODEGRADABILITY CASE STUDY: PLASTICS
Synthesis of PolyLactic Acid (PLA) from starch
Advantages
Has PET performance
Made from renewable materials
Biodegradable in the environment

## Slide 58: PRINCIPLE 11 Analytical methodologies need to be further developed to allow for real-time, in-process monitoring and control prior to the formation of hazardous substances.

## Slide 59: ROLE OF ANALYTICAL CHEMISTRY
Analytical chemistry has been at the heart of the environmental movement since its inception. It’s been used in:
    Identification
    Monitoring
    Measurement
    Characterization

## Slide 60: GREEN ANALYTICAL CHEMISTRY
Green Chemistry is applicable to all chemical processes, including the methods, protocols and processes of environmental analytical chemistry.
Source: Wikipedia

## Slide 61: EXAMPLES OF GREEN ANALYTICAL CHEMISTRY METHODOLOGIES
Supercritical Fluid Extraction
X-ray fluorescence detection for multi-metal matrix
Solid-phase extraction and micro-extraction

## Slide 62: PROCESS ANALYTICAL CHEMISTRY TO PREVENT POLLUTION
Through the use of real-time, in-process monitors, sensors, etc., pollution and hazardous waste generation can be prevented rather than simply measured after it is produced.

## Slide 63: PRINCIPLE 11: REAL-TIME MONITORING CASE STUDY: ISOBUTANE ALKYLATION
Solid-acid catalyzed 1-butene/isobutane alkylation process
  replaces HF and H2SO4 catalysts
  process utilizes supercritical CO2 to prevent coke accumulation in pores of solid catalyst
  on-line GC analysis
Subramaniam, University of Kansas

## Slide 64: PRINCIPLE 12 Substances and the form of a substance used in a chemical process should be chosen so as to minimize the potential for chemical accidents, including releases, explosions, and fires.

## Slide 65: PRINCIPLE 12: MINIMIZE HAZARD
Accidents can be avoided by minimizing hazard.
Approaches to design safer chemistry can include the use of solids or low vapor pressure substances in place of volatile liquids.
Other approaches include avoiding the use of molecular halogens in large quantities.

## Slide 66: PRINCIPLE 12: MINIMIZE HAZARD
Designing safer polymers for use in airplanes
Polyhydroxyamide (PHA): synthesized under mild conditions, moldable into seats, bins, wall panels decomposes into fire-resistant polybenzoxazole (PBO) and water upon heating
  Westmoreland, UMass Amherst

## Slide 67: GREEN CHEMISTRY PRINCIPLES AND LIFE-CYCLE
Chem. Soc. Rev., 2015, 44, 5758-5777

## Slide 68: THANK YOU!
QUESTIONS?
This training material was developed in close collaboration with the Center for Green Chemistry and Green Engineering at Yale University.
www.greenchemistry-toolkit.org